TTGO TDISPLAY PINOUT

LORANOW connecions

Połączenie Koncentartor V3

LORA RFM 98

RFM97	- ESP32
MISO	-	15
MOSI	- 13
SCK	- 12
SS	- 17
DIO0	- 2

DS18B20
DQ	-	32

MCP23017

SDA	-	21
SCL	-	22

Zmiany bibliotek:
1.Zmieniono domyślne ustawienia biblioteki spi dla esp32 – tworzony domyślnie obiekt SPI jest podłączony do HSPI a nie VSPI
2. Zmieniono domyślny adres urządzeń MCP23XXX – plik C:\Users\mirsmok\Documents\Arduino\libraries\Adafruit_MCP23017_Arduino_Library\src\Adafruit_MCP23XXX.h linia 27 :
#define MCP23XXX_ADDR 0x20 //!< Default I2C Address
na
#define MCP23XXX_ADDR 0x27 //!< Default I2C Address

Zmiana w blibliotece PubSubClient
funkcja connect dodany zmieniony timeout
        _client->setTimeout(500);

Zmiany w bibliotece Lora przy read dodano ograniczenie ilości znaków oraz dodano atrybuty do przerwań

ESP32 GPIO CONFIG

GPIO	Input	Output	Notes
0	pulled up	OK	outputs PWM signal at boot
1	TX pin	OK	debug output at boot
2	OK	OK	connected to on-board LED
3	OK	RX pin	HIGH at boot
4	OK	OK
5	OK	OK	outputs PWM signal at boot
6	x	x	connected to the integrated SPI flash
7	x	x	connected to the integrated SPI flash
8	x	x	connected to the integrated SPI flash
9	x	x	connected to the integrated SPI flash
10	x	x	connected to the integrated SPI flash
11	x	x	connected to the integrated SPI flash
12	OK	OK	boot fail if pulled high
13	OK	OK
14	OK	OK	outputs PWM signal at boot
15	OK	OK	outputs PWM signal at boot
16	OK	OK
17	OK	OK
18	OK	OK
19	OK	OK
21	OK	OK
22	OK	OK
23	OK	OK
25	OK	OK
26	OK	OK
27	OK	OK
32	OK	OK
33	OK	OK
34	OK		input only
35	OK		input only
36	OK		input only
39	OK		input only

Continue reading for a more detail and in-depth analysis of the ESP32 GPIOs and its functions.
### Input only pins
GPIOs 34 to 39 are GPIs – input only pins. These pins don’t have internal pull-up or pull-down resistors. They can’t be used as outputs, so use these pins only as inputs:

Those internal touch sensors are connected to these GPIOs:
- T0 (GPIO 4)
- T1 (GPIO 0)
- T2 (GPIO 2)
- T3 (GPIO 15)
- T4 (GPIO 13)
- T5 (GPIO 12)
- T6 (GPIO 14)
- T7 (GPIO 27)
- T8 (GPIO 33)
- T9 (GPIO 32)
Learn how to use the touch pins with Arduino IDE: ESP32 Touch Pins with Arduino IDE
### Analog to Digital Converter (ADC)
The ESP32 has 18 x 12 bits ADC input channels (while the ESP8266 only has 1x 10 bits ADC). These are the GPIOs that can be used as ADC and respective channels:
- ADC1_CH0 (GPIO 36)
- ADC1_CH1 (GPIO 37)
- ADC1_CH2 (GPIO 38)
- ADC1_CH3 (GPIO 39)
- ADC1_CH4 (GPIO 32)
- ADC1_CH5 (GPIO 33)
- ADC1_CH6 (GPIO 34)
- ADC1_CH7 (GPIO 35)
- ADC2_CH0 (GPIO 4)
- ADC2_CH1 (GPIO 0)
- ADC2_CH2 (GPIO 2)
- ADC2_CH3 (GPIO 15)
- ADC2_CH4 (GPIO 13)
- ADC2_CH5 (GPIO 12)
- ADC2_CH6 (GPIO 14)
- ADC2_CH7 (GPIO 27)
- ADC2_CH8 (GPIO 25)
- ADC2_CH9 (GPIO 26)